Principle and Maintenance of DK1017S

CONTENTS

Chapter I Overview of DK1017S

- Description of Functions

- Block Diagram of Player

3、Composition of IC for Player

Chapter II Operating Principle of Servo Circuit

- Processing Procedure of Digital Signal

2、Processing Procedure of Control Signal

Chapter III Operating Principle of Decoding Circuit

- Control Circuit of System

- Audio and Video Output Circuit

Chapter IV Operating Principle of Power Board

1、Block Diagram

2、Operating Principle of Circuits

Chapter V Operating Principle of Panel

1. Operating Principle

Chapter VI Troubleshooting

Appendix: Functions of IC Pins

#### Schematic & PCB wiring diagram

Spare parts list

Important prompt:

This type player employs two kinds of decks, SF-HD62 and SF-HD60, and corresponding software of these two types of decks are different, therefore please pay special attention during deck changing in the maintenance. Corresponding decks should be changed with the same type of original ones, otherwise the player will be out of order. Identification of decks is shown as figures:

Operating Principle Analysis of DK1017S

Chapter I Overview of DK1017S

DK1017S is a medium- low-grade model integrating with video disc and power amplifier, with the following major features:

1. The layer adopts “Sanyo loader+MT1389” solution;

2.  The power amplifier adopts the digital power amplification circuit, with the power IC of TAS5112DFD; it has low distortion level;

3. The audio process adopts TAS5508 , with high integration and high performance and price ratio;

4. It has the function of radio reception, and the tuner adopts Sanzhenxing DTS-44K（CE）module;

5. The power supply adopts the switching power, with compactness, high efficiency and stable performance;

6. Equipped with SCART（CVBS/RGB）port;

7. Accessory channel input/output function;

8. Headphone output function;

9. Karaoke and automatic accompaniment function

10. “RDS” function;

### II. Block Diagram of DK1017S Complete Player and IC Function Table:

III. Function Table of ICs for DK1017S

| Circuit Board | No | Name | Function |
| --- | --- | --- | --- |
| Deck |  | Sanyo | Pick-up of disc signal |
| Main Board | U201 | MT1389 | RF signal processing, digital signal processing, servo processing, MPEG decoding, line scan, system control |
|  | U202 | AT24C02 | Series EEPROM, status memory |
|  | U205 | HCU04 | Hex inverter |
|  | U209 | LM1117MP-1.8 | 1.8v voltage-regulated power supply |
|  | U211 | AE45164016 | 64Mbit SDRAM |
|  | U214 | 29LV160BE | 16Mbit FLASH ROM |
|  | U302 | D5954 | 4-channel servo driver circuit |
| Panel | N102 | S0793 | Panel control, VFD display drive |
|  | N103 | REMOT | Remote receptor |

| Power Board | U501 | 0380 | Switching power circuit |
| --- | --- | --- | --- |
|  | U502 | HS817 | Photo-electric coupler |
|  | U503 | HA17431 | 2.5V reference voltage comparator |
|  | U11 | LM7805 | 5V 3-terminal voltage-regulated power supply |
|  | U505 | 0880 | Switching power circuit |
|  | U506 | HS817 | Photo-electric coupler |
|  | U507 | LM431 | 2.5V reference voltage comparator |
| Amplifier board | N12 | 5508 | Digital signal processing |
|  | N13/14 | 5112 | Power amplification |
|  | N8/9 | TLV272 | Operational amplification |
|  | N10/11 | RC4580 | Digital signal amplification |

### Chapter II Operating Principle of Servo Circuit

### I.  Digital Signal Processing Procedure

DK1017S adopts Sanyo double beam super error correction deck and MTK decoding solution, and its servo circuit mainly consists of preposition signal processing, digital servo processing, digital signal processing IC MT1389 and driver circuit BA5954. MT1389 is also a main part of the decoding circuit.

The A, B, C, D, E, F, SA, SB and RFO signal transmitted from the deck are mainly inputted through the 2-13 pins of MT1389, and after amplifying treatment of built-in amplifier of MT 1389, the signals are treated in two parts within MT1389:

After being processed by the internal digital servo signal circuit of MT1389, part of the signal forms into corresponding servo control signal, and output focus (FOSO), tracking (TRSO), main shaft (DMSO) and feed (FMSO) servo control signal from the P42, P41, P37 and P38 of MT1389 and send them to the driver circuit BA5954 to amplify the drive. After drive amplification, the signals will drive the focus coil, tracking coil, main shaft motor and feed motor. The focus and tracking servos will be used to adjust the object lens and enable laser beam to identify signal from compact disc correctly; the feed servo will be used to drive the laser head to move longitudinally, and scan the compact disc; the main shaft servo is used to control the main shaft motor to read the signals in constant linear speed and drive the disc to rotate.

After being processed by the internal VGA voltage-controlled amplifier of MT1389 in amplification and balance frequency compensation; another part of the signals is converted into digital signal by the internal A/D converter. When the deck reads the CD/VCD signals, these signals will be EFM demodulated in MT1389, and after accomplishing CIRC error regulation in internal MT1389, output to the next grade to carry out audio and video decoding; when the deck reads the DVD signals, these signals will be ESM demodulated in MT1389, and after accomplishing RSPC error regulation in internal MT1389, output to the next grade to carry out audio and video decoding.

II. Processing Procedure of Control Signal

1. Automatic control of laser power, with the circuit shown as the Figure II:

Figure II

MT1389 is integrated with APC (automatic light power control) circuit. Its Pin 20 is the pin for inputting VCD laser power rate detection signal, the Pin 21 is the pin for inputting DVD laser power rate detection signal, and the Pin 23 is the pin for outputting VCD laser power rate drive control. When the Pin 23 finds that the laser output power rate is too strong, the output voltage on Pin 23 will increase after the processing of internal circuit of MT1389, and then the conduction degree of V302 (2SB1132) and the voltage on its integration polar will decrease, which consequently lead to the decrease of voltage supplied to the laser tube, the weakening of laser head lighting, and thus achieve the automatic adjustment on laser output power. The Pin 22 is the pin for outputting DVD laser power drive control, with the specific control procedure similar to that of VCD.

2. The tray open/close control circuit is shown as the Figure III:

Figure III

Different from the circuit in former MTK solution, the MT1389 is integrated with preposition signal processing circuit, so the tray open/close control signals are accomplished by MT1389, that is to say, the close control signal is accomplished by the Pin 51 of MT1389, while the open control signal by Pin 39 of MT1389.

When we press the open button, the Pin 51 of MT1389 is in high power level, while the Pin 39 is in low power level, and then the triode V308 will be on-state. Through resistor R323, the base of V306 will be made to be in low power level, and V306 will be on-state, with the current direction as the following figure:

Power voltage VCC →V306E-C junction →motor negative terminal LOAD- → motor positive Load +→V308 C-E junction → grounding

So the motor will rotate clockwise to accomplish the action of tray closing.

When we press the open button, the Pin 51 of MT1389 is in low power level, while the Pin 39 is in high power level, and then the triode V307 will be conducted. Through resistor R324, the base of V309 will be made to be in low power level, and V309 will be conducted, with the current direction as the following figure:

Power voltage VCC →V309E-C junction →motor negative terminal LOAD- → motor positive Load +→V307 C-E junction→ grounding

So the motor will rotate anti-clockwise to accomplish the action of tray opening.

3. The main shaft motor braking circuit is as the Figure IV:

To prolong the lifespan of motor and reduce the influence of start-up impact current, with the installation of disc, our R&D personnel design the main shaft motor to be in the state of constant operation, so that even if the STOP button is pressed, the disc will not be stopped. Therefore, when we press the OPEN button, a braking signal is required to stop the rotation of main shaft motor immediately to accomplish the opening action in a short time.

Figure IV

During playing, if we press the OPEN button, the main shaft drive signal will disappear, and because of inertia, the main shaft motor is still in operation. As the electromotive force generated in the operation of motor receives the induction voltage on sampling resistors R321 and R340, which, through the resistor R319 and R320, is added to the Pin 36 and Pin 35 of MT1389, and outputted from the Pin 34 after internal processing for amplification in MT1389, and delivered to Pin 47 of MT1389 through R318. After the internal A/D conversion and corresponding processing, an instant motor reversal braking signal will be outputted from the Pin 37 of MT1389 to stop the rotation of main shaft motor immediately, so as to ensure the standstill of the disc when opening the player.

### III. Servo drive circuit

The servo drive of the player is accomplished through a piece of 4-channel dedicated drive circuit BA5954, with the circuit as Figure V:

The 4 servo control signals generated in digital servo circuit processing of MT1389, i.e. focusing control FOSO, tracking control TRSO, feed control FMSO and main shaft control DMSO signals, are added to the pins 1, 26, 23 and 5 of BA5954 respectively, and after drive amplification of BA5954, the focusing and tracking drive signals will be outputted from the pins 13 and 14 and pins 15 and 16 of BA5954 respectively, and added to the focusing and tracking coils to drive the light head to accomplish the actions of focusing and tracking.

The feed and main shaft drive signals will be outputted from the pins 17 and 18 and pins 11 and 12 of BA5954 respectively, and added to the feed motor and main shaft motor to drive the light head to move longitudinally and enable the disc to rotate in constant linear speed.

The STBY on Pin 28 of BA5954 is an output-enabling signal, and only when the pin is in high power level, there will be output of drive voltage on the output terminal.

Chapter III Operating Principle of Decoding Circuit

The decoding circuit of the player mainly consists of decoding chips (including MT1389, SDRAM AE45164016 and FLASH ROM 29LV160BE) and audio DAC CS4360.

### I. Control Circuit of System

1. Reset circuit is as the Figure VI:

Figure VI

The reset circuit of the player consists of triode Q204 9014, reset capacitor TC217 100uF/16V and phase inverter U205 HCU04. In starting up, as the terminal voltage of capacitor cannot be changed suddenly, the basic of Q204 is in low power level. After the cut-off of Q204, its emission polar is in low power level, after secondary phase inversion by U205 and regulation, the low power level reset signal is outputted to the Pin 110 of MT1389 to reset MT 1389.

When the recharging of TC217 is finished, the base of Q204 will be in high power level, Q204 will be conducted, and the emission polar is in high power level. After the secondary phase inversion and regulation by U205, a high power level is outputted and added to the Pin 110 of MT1389 to maintain high power level during its normal operation.

2. Clock circuit

The crystal oscillator of X201 27MHz, C275/27PF, C276/27PF and phase inverter HCU04 form into clock oscillation circuit, and the clock signals generated are added to the pins 229 and 228 of MT1389 through R244 and 4248 to provide operating clock for MT1389.

3. Data communication circuit

The data communication circuit of the player consists of decoding chip MT1389, SDRAM, AE45164016 and FLASH ROM 29LV160BE, as the Figure VII:

MT1389 is a piece of super large integrated circuit, with the operation voltage of +3.3V and +1.8V. Its functions include: RF small signal preposition processing, digital servo, digital signal processing and accomplishing MPEG decoding and video coding. The built-in MCU of MT1389 is also the system control circuit of the whole player.

AE45164016 is a piece of 4M*16bit large capacity SDRAM, with the operation voltage of +3.3 V. In DV971, the 6ns module is adopted, with high speed and the maximum operation frequency up to 166MHz. Its main function is for operation buffer storage of decoding chip MT1389 to store the audio and video data stream in decoding.

29LV160BE is a piece of 16Mbit FLASH ROM, with the operation voltage of +3.3V, mainly for storing the user’s information including OSD character information, operational microcode and LOGO in start-up.

II. Audio and Video Output Circuit

1. Video output circuit

DK1017S can not only output three types of alternating-line video signal (including CVBS composite video, S terminal Y-C signal and Y/Cb/Cr color difference signal), but also output two types of progressive line video signal (including Y/Pb/Pr progressive line color difference signal and VGA progressive line signal).

The decoding chip MT1389 has built-in video encoding circuit for direct output of analogue composite video signal CVBS, S terminal, color difference signal and VGA signal.

The CVBS composite video signal is outputted from the Pin 198 of MT1389, the S terminal signal Y-C is outputted from the pins 194 and 196 of MT1389, the color difference signal and the R-B-G signal of VGA port is outputted from the pins 203, 202 and 200 of MT1389, the row and field synchronization signals of VGA port are outputted from the pins 207 and 205 of MT1389 respectively.

To mention specifically, the alternating-line color difference signal, the progressive line color difference signal and progressive line R-B-G signal are outputted from the same pin, therefore the signal output shall be selected according to the ports of TV, otherwise there will be only sound but without picture display.

2. Audio output circuit

Audio signals processed by MT1389 output 5-track data signals through pin 217, pin 218 and pin 219 and 5-channel clock signals through pin 214 and pin 215. These signals after passing through IC 74HCT125 are transmitted to audio signal processing IC TAS5508 to be processed (specific IC data please refer to Attachment), then 10 groups of PWM signals are output, six of which are transmitted to power amplifying parts, two of which to headphone output and two of which to auxiliary channel output.

Six groups of signals transmitted to power amplifying IC are processed by surrounding and super DBB sharing an N13 IC TAS5508, and by main sound channel and center sharing an N14 IC TAS5508. Signals are amplified here, for they are digital high frequency signals, they have high efficiency; meanwhile power IC has low colorific value. Amplified signals are still digital signals, in order that they can be output through loudspeaker, amplified digital signals still have to be processed before outputting.

For PWM signals containing audio signals, since high frequency signals have high frequency and are beyond audibility range of human ears, we can ignore impacts of high frequency signals and reduce low frequency audio signals only during processing.

TAS5508 is an 8-channel pulse width modulated high performance IC, and applicable in processing most digital audio signals. Between 20Hz and 20KHz, it has excellent noise factor and dynamic range. It has following features:

- Automatically control clock speed and digital sampling speed;

- 8 groups of audio input channels;

- 8 groups of PWM output can be changed into 6-channel stereo line output or 8-channel line output;

- Line output is a different input open loop amplifier driven by a group of PWM signals.

IC TAS5112 is a high performance audio power amplifier. Bridging with 6Ω loading, each channel can output 50W. It has 95DB dynamic range, low distortion degree and low rate of heat generation with power efficiency up to 90%. It also has functions of low-voltage protection, high-temperature protection, overflow protection, etc. At the same time, it has built-in driving power adjustment gate circuit. It is applicable in family video, DVD receiver, mini music center, etc. Detailed IC introduction see Attachment.

When in normal disc reading, digital signals and clock signals from 1389 are transmitted to pin 26 to pin 31 of IC TAS5508 through IC 74HCT125 gating. If no headphone is inserted, PH-SEL is of high level, as well as when MUTE is normal. And pin 37 of TAS5508 is also of high level. All data lines and clock lines can be detected by oscilloscope. One group of signals from 5508 is transmitted to N8 and N9, then output through auxiliary channel. Another group is transmitted to headphone; other PWM signals are transmitted to amplifying parts of amplifier.

When headphone is inserted, PH-SEL signal is forcibly shorted to earth, and turns to low level, meanwhile amplifier is muted.

This amplifier has functions of radio reception, auxiliary channel output and karaoke. All external inputs after N3 CD4052 gating and N7 CS5340 analog-to-digital conversion are transmitted to MT1389. Rear processing and output is the same as the signal output flow in normal disc reading.

When in disc reading, system defaults to gate karaoke input, therefore you can open karaoke when playing disc. This amplifier also has automatic accompaniment function, when playing VCD, system detects external input and automatically screen to human sound signal in the disc, while only saves sound accompaniment.

DK1017S has the function of radio reception, and can also receive RDS signal. The radio head control lines CE, DI, CL and DO are controlled by 28 array lines connecting to MT1389 control. When any of the controlling lines is in abnormality, the radio reception will be in malfunction. The RDS signal received by radio head will be delivered to the dedicated IC SAA6588 for processing.

Chapter IV Operating Principle of Power Board

I.  Block Diagram

This amplifier has two groups of power supply; one is of low voltage for decoding board and low power ICS, the other is of higher voltage for power amplifying IC. But their design principles, we only draw one functional block diagram of them:

II. Introduction of Circuit Principle

220V alternating current is loaded on D501-D504 integrated bridging rectification circuit through power plug, fuse tube, voltage dependent resistor R501 and common mode rejection BC501 and L501. Diode adopts IN4007 which ahs better PPR and higher withstand voltage value than IN4001. Output 311V direct current after being bridging rectified is loaded on two transformers through TC501 filtering and transmitted to DRAIN control pins of switch modules U501 and U502.

Service voltage of power on IC after being directly rectified and filtered is divided by resistors to serve IC. Diode D508, capacitor C516 and resistor R516 form absorption circuit to provide discharge circuit of reverse electromotive force for 1-4 coils of transformers. Pin FB controlling IC is feedback control pin, so you should decide on/off time of pulse width according to current intensity on it to ensure stability of output voltage.

There are 5 branch circuits coupled to sub-grade through transformer.

- Voltage output from pin 11 and pin 13 of transformer T501 outputs a group of +28V voltage for power amplifying IC after being rectified and filtered.

- Voltage output from pin 16 of transformer T501 outputs a group of +12V voltage after being rectified and filtered. +12V voltage is stabilized into a group of +5V voltage by IC LM7805.

- Voltage output from pin 14 of transformer T501 outputs +5V voltage and provide voltage for one end of photo-electric coupler U502 after being rectified and filtered.

- Voltage output from pin 12 of transformer T501 outputs +3.3V voltage and provide a group of stable voltage for CPU after being rectified and filtered.

- Voltage output from pin 9 of transformer T501 outputs a group of 21V voltage for displaying driving IC after being rectified and filtered. Clamp ZD501 of -21V provide heater voltage for panel display screen. Grounding direct voltage of FL+ and FL- is about -16V.

Operating principles of two groups of switch power are the same, therefore we will only analyze the group providing +3.3V voltage for CPU here:

Feedback sampling of this group comes from 3.3V and supplies for photocupler HS817 through D516 and R506. At the same time, it is divided through R508 and R509 for reference voltage pin R of 2.5V comparator. When 3.3V becomes higher, pin KA of comparator is on; and the voltage is transmitted to pin 4 of switch IC 5L0380R after photoelectric coupling through HS817 to reduce on time of internal switch tube. And thus it reduces transformer coupling and decreases output of 3.3V voltage to achieve automatic adjustment and control, and vice verse.

It has to be noted that in this switching power reference voltage comparator IC of two groups of switching power are different. For voltage of the group supplying power for amplifier is higher, it adopts LM431 which has better performance and higher withstand voltage. And voltage of the group supplying power for 3.3V is lower, it adopts 17431. For two ICs are different, you should pay special attention to distinguish them from each other. They cannot be used mixing.

## Chapter 5: Panel control and VFD display circuit

The panel mainly consists of VFD screen, driver IC0793, remote receptor HS0038A2 and button and indicator display circuit, mainly for accomplishing man-player dialogue and display of operation status.

The structural drawing is as follows:

Figure XI

MT1389 will control the U401 IC 0793 to display the operation status of the player through the VFDST status, VFDCK clock and VFDAT data, under the control of CPU built in MT1389, receive the user control commands sent by UPD16312, and control the controlled circuit of the player to limit the player to operate in specified status.

When the user operates the panel buttons, the control command is sent to the IC 0793 through keyboard-scanning circuit, and through internal decoding drive, the IC 0793 outputs the control data from the pins 5 and 6 (VFDAT) to the built-in CPU of MT1389, which will realize the control on the controlled circuit, and control the VFD through IC 0793.

VFD401 is a vacuum fluorescence screen, and its biggest feature is its high brightness. Its operation principle is similar to the kinescope of TV. The pins 1, 2, 34 and 35 are for filament power supply; the pins 27-32 are GRID poles, each GRID has 16 different characters of display; the pins 4-19 are SEG poles, and the CPU control the SEG poles through its control on IC 0793, and display the characters of corresponding operation status on the screen.

The remote reception circuit mainly consists of remote receptors HS0038A2, of which the pin 1 is for grounding, the pin 2 for power supply, the pin 3 for output of reception signal, and they are all connected directly to the CPU in MT1389 to control the corresponding circuit.

This player has headphone output function. A pin in the headphone directly connects to TAS5508. When the headphone is inserted, detection line H-DET grounds and turns into low level. When pin 12 of TAS5508 turns into low level, parts of output of amplifier are muted. When in normal condition, this detection pin is of high level around 3.3V.

### Troubleshooting

### I. Voltage on key points of DK1017S

Demoding circuit:

Reset:

1. U205 (HCU04): 8 pins, around 5V;

2. MT1389: 110 pins, around 5V;

3. FLAHS ROM: 12 pins, around 5V

Clock:

27MHZ crystal oscillator two ends: Around 0.77V.

I2C bus SDA: 3.3V

I2C bus SCL  3.3V

Servo circuit:

LD01： 3.3V；LD02：3.3V

V301 and V302 electron collector LD voltage: 2.3V

BA5954 pin 4 base voltage: 1.4V

BA5954 pins 15 and 16 tracking drive output: Around 2.5V

BA5954 pins 17 and 18 feed drive output: Around 2.5V

BA5954 pins 13 and 14 focus drive signal output: Around 2.5V

BA5954 pins 11 and 12 main shaft drive output: Around 2.5V

BA5954 pin 1 focus control signal input: 1.4V

BA5954 pin 5 main shaft control signal input: 1.4V

BA5954 pin 26 tracking control signal input: 1.4V

BA5954 pin 23 feed control signal input: 1.4V

Amplifier circuit：

TAS5508  pin 9 power supply pin 3.3V

TAS5112  32、33、40、41、44、45、52、53, 28V。\

### II. Troubleshooting of main troubles

NO

YES

NO

YES

NO

YES

NO

YES

YES

YES

NO

NO

YES

YES

YES                     NO

NO

YES

YES	YES

NO

YES

YES

YES

NO

# Attachment ：Brief Introduction to IC Pins

### I. MT1389

MT1389 adopts the LQFP 256 pin packaging and 3.3V/1.8V double voltage operation mode. It is a piece of large-scale CD-ROM and DVD-ROM preposition processing CMOS integrated circuit with excellent performance, and a single chip dedicated to CD/VCD/DVD player. It contains focusing servo error amplification, tracking servo error amplification and RF level output servo control, including the following main functions:

RF small signal preposition processing, mainly for carrying our corresponding processing and amplification on the RF signals transmitted from the light head part, adjusting the laser output power automatically, and identifying the VCD disc and DVD disc.

Digital servo processing can generate focusing, tracking, feed and main shaft servo control signals; digital signal processing, accomplishing the EFM/EFM + demodulating of RF signals.

MPEG-1/MPEG-2/MPEG4/JPEG Video decoding chip, which can not only realize the decoding of VCD and DVD, but also realize MPEG 4 network video decoding, being compatible to “network movie” disc, and decipher JPED pictures to realize the function of digital photo album play.

On audio aspect, it can not only realize AC-3/DTS double decoding, decipher MP3, and is also compatible to DVD-Audio decoding to achieve high-resolution sound restoration in 1000 times higher than CD.

By utilizing the 8032 microprocessor with built-in chip, MT1369E can also realize the system control function of player, which simplifies the circuit design substantially.

The pin functions of MT1389 are as the following table:

| Pin | Name | Function |
| --- | --- | --- |
| 1 | AGND | Analogue grounding |
| 2 | DVDA | DVD-RF high-frequency AC coupling signal A |
| 3 | DVDB | DVD-RF high-frequency AC coupling signal B |
| 4 | DVDC | DVD-RF high-frequency AC coupling signal C |
| 5 | DVDD | DVD-RF high-frequency AC coupling signal D |
| 6 | DVDRFIP | DVD-RF high-frequency AC coupling signal RFIP input |
| 7 | DVDRFIN | DVD-RF high-frequency AC coupling signal RFIN input |
| 8 | MA | DVD-RAM main light beam RF DC signal input A |
| 9 | MB | DVD-RAM main light beam RF DC signal input B |
| 10 | MC | DVD-RAM main light beam RF DC signal input C |
| 11 | MD | DVD-RAM main light beam RF DC signal input D |
| 12 | SA | DVD-RAM auxiliary light beam RF DC signal input A |
| 13 | SB | DVD-RAM auxiliary light beam RF DC signal input B |
| 14 | SC | DVD-RAM auxiliary light beam RF DC signal input C |
| 15 | SD | DVD-RAM auxiliary light beam RF DC signal input D |
| 16 | CDFON | CD focusing error phase inversion input |
| 17 | CDFOP | CD focusing error phase input |
| 18 | TNI | 3 light beam auxiliary PD signal phase inversion input |
| 19 | TPI | 4 light beam auxiliary PD signal phase input |
| 20 | MDI1 | Laser power monitoring input 1 |
| 21 | MDI2 | Laser power monitoring input 2 |
| 22 | LDO2 | Laser power monitoring output 2 |
| 23 | LDO1 | Laser power monitoring output 1 |
| 24 | SVDD3 | Servo 3.3V power supply |
| 25 | CSO/RFOP | Main servo signal output/RF phase output |
| 26 | RFLVL/RFON | RF level output/RF phase inversion output |
| 27 | SGND | Servo grounding |
| 28 | V2REFO | Reference voltage 2.8V |
| 29 | V20 | Reference voltage 2.0V |
| 30 | VREFO | Reference voltage 1.4V |
| 31 | FEO | Focusing error signal output |
| 32 | TEO | Tracking error signal output |
| 33 | TEZISLV | Tracking zero crossover error input |
| 34 | OP_OUT | Sensing signal amplification output |
| 35 | OP_INN | Sensing signal phase inversion input |
| 36 | OP_INP | Sensing signal non-inverting input |
| 37 | DMO | Main shaft control signal output |
| 38 | FMO | Feed control signal output |
| 39 | TROPEN PWM | Tray Open signal output |
| 40 | PWMOUT1/ADIN9 | First-route pulse width demodulating signal output/AD universal input |
| 41 | TRO | Tracking control signal output |
| 42 | FOO | Focusing control signal output |
| 43 | USB_VSS | USB grounding |
| 44 | USBP | USB data |
| 45 | USBM | USB data |
| 46 | USB_VDD3 | USB 3.3V power supply |
| 47 | FG/ADIN8 | Motor sensing signal input/AD universal input |
| 48 | TDI/ADIN4 | Open position detecting signal input/AD universal input |
| 49 | TMS/ADIN5 | Close position detecting signal input/AD universal input |
| 50 | TCK/ADIN6 | BA5954 enabling signal output/AD universal output |
| 51 | TDO/ADIN7 | Tray close signal output/AD universal input |
| 52、97、122、152、173、221 | DVDD18 | Digital 1.8V power supply |
| 53-58 | IOA2-7 | Micro-controller address bit 2-7 |
| 59 | HIGHA0 | Micro-controller address bit 0 |
| 60、61 | IOA18-19 | Micro-controller address 18-19 |
| 62、85、94、116、119、134、144、148、161、163、175、216、223 | DVSS | Digital grounding |
| 63 | APLLCAP | Analogue phase lock loop external capacitor |
| 64 | APLLVSS | Analogue phase lock loop grounding |
| 65 | APLLVDD3 | Analogue phase lock 3.3V power supply |
| 66 | IOWR | FLASH read control signal |
| 67-72 | HIGHA3-7 | Micro-controller address bit 3-7 |
| 73、80、108、127、141、155、167、182、204、212 | DVDD3 | Digital 3.3V power supply |
| 74、75 | HIGHA1-2 | Micro-controller address bit 1-2 |
| 76 | IOA20 | Micro-controller address bit 20 |
| 77 | IOCS | FLASH chip selection |
| 78 | IOA1 | Micro-controller address bit 1 |
| 79 | IOOE | FLASH output enabling |
| 81-84 | AD0-3 | Micro-controller address/data bit 0-3 |
| 86-88 | AD4-6 | Micro-controller address/data bit 4-6 |
| 89 | IOA21/ADIN0 | Micro-controller address bit 21/AD universal input |
| 90 | ALE | Micro-controller address enabling |
| 91 | AD7 | Micro-controller address/data bit 7 |
| 92 | A17 | FLASH address bit 17 |
| 93 | IOA0 | Micro-controller address bit 0 |
| 95 | UWR | Micro-processor reading operation |
| 96 | URD | Micro-processor reading operation |
| 98 | UP1_2-1_7 | Micro-processor port |
| 104 | UP3_0 | Micro-processor port |
| 105 | UP3_1 | Micro-processor port |
| 106 | UP3_4 | Micro-processor port |
| 107 | UP3_5 | Micro-processor port |
| 109 | ICE | Micro-processor correction mode enabling |
| 110 | PRST | Reset input |
| 111 | IR | Remote control signal input |
| 112 | INT0 | Micro-processor interruption 0 |
| 113 | DQM0 | DRAM input output shielding signal |
| 114 | DQS0 | DRAM input output shielding signal |
| 115 | RD7 | DRAM data |
| 117-118 | RD5-6 | DRAM data |
| 120-121 | RD3-4 | DRAM data |
| 123-125 | RD0-2 | DRAM data |
| 126 | RD15 | DRAM data |
| 128-133 | RD9-14 | DRAM data |
| 135 | RD8 | DRAM data |
| 136 | DQS1 | DRAM input output shielding signal |
| 137 | DQM1 | DRAM input output shielding signal |
| 138 | RWE | DRAM writing enabling |
| 139 | CAS | DRAM column address selection |
| 140 | RAS | DRAM row address selection |
| 142 | RCS | DRAM chip selection |
| 143 | BA0 | DRAM section address 0 |
| 145 | BA1 | DRAM section address 1 |
| 146 | RA10 | DRAM address |
| 147 | RA0 | DRAM address |
| 149 | RA1-3 | DRAM address |
| 153 | RVREF/ADIN3 | Reference voltage/AD universal input |
| 154 | RCLKB | DRAM clock |
| 156 | RCLK | DRAM clock |
| 157 | CKE | DRAM clock enabling |
| 158 | RA11 | DRAM address |
| 159-160 | RA8-9 | DRAM address |
| 162 | RA7 | DRAM address |
| 164 | RA4-6 | DRAM address |
| 168 | RD13/ASDATA5 | DRAM data/audio series data |
| 169 | RD27-30 | DRAM data |
| 174 | RD26 | DRAM data |
| 176-177 | RD24-25 | DRAM data |
| 178-179 | DQM2-3 | DRAM I/O shielding signal |
| 180-181 | RD22-23 | DRAM data |
| 183-188 | RD16-21 | DRAM data |
| 189 | DACVDDC | D/A conversion 3.3V power supply |
| 190 | VREF | Reference voltage |
| 191 | FS |  |
| 192 | YUV0/CIN |  |
| 193 | DACVSSC | D/A conversion grounding |
| 194 | YUV1/Y | Video signal YUV1 output/Y signal output |
| 195 | DACVDDB | D/A conversion 3.3V power supply |
| 196 | YUV2/C | Video signal YUV2 output/C signal output |
| 197 | DACVSSB | D/A conversion grounding |
| 198 | YUV3/CVBS | Video signal YUV3 output/CVBS signal output |
| 199 | DACVDDA | D/A conversion 3.3V power supply |
| 200 | YUV4/G | Video signal YUV4 output/G signal output |
| 201 | DACVSSA | D/A conversion grounding |
| 202 | TUV5/B | Video signal YUV5 output/B signal output |
| 203 | YUV6/R | Video signal YUV6 output/R signal output |
| 205 | VSYNC/ADIN1 | Field synchronization signal output/AD universal input |
| 206 | YUV7/ASDATA5 | Video signal YUV7 output/audio series data |
| 207 | HSYNC/ADIN2 | Row synchronization output/AD universal input |
| 208 | SPMCLK |  |
| 209 | SPDATA |  |
| 210 | SPLRCK |  |
| 211 | SPBCK/ASDATA5 |  |
| 213 | ALRCK | Audio left and right sound channel clock |
| 214 | ABCK | Audio bit clock |
| 215 | ACLK | Audio DAC external clock |
| 217-220 | ASDATA0-3 | Audio series data |
| 222 | ASDATA4 | Audio series data |
| 224 | MC_DATA | Microphone digital audio input |
| 225 | SPDIF | Digital audio signal output |
| 226 | RFGND18 | RF signal grounding |
| 227 | RFVDD18 | RF signal 1.8V power supply |
| 228 | XTALO | Clock output |
| 229 | XTALI | Clock input |
| 230 | JITFO | RF small signal output |
| 231 | JITFN | RF small signal phase inversion and amplification input |
| 232 | PLLVSS | Phase lock loop grounding |
| 233 | IDACEXLP |  |
| 234 | PLLVDD3 | Phase lock loop 3.3V power supply |
| 235 | LPFON | Amplifier loop wave filtration output |
| 236 | LPFIP | Amplifier loop wave filtration input |
| 237 | LPFIN | Amplifier loop wave filtration input |
| 238 | LPFOP | Amplifier loop wave filtration output |
| 239 | ADCVDD3 | A/D conversion 3.3V power supply |
| 240 | S_VCM |  |
| 241 | ADCVSS | A/D conversion grounding |
| 242 | S_VREFP |  |
| 243 | S_VREFN |  |
| 244 | RFVDD3 | RF 3.3V power supply |
| 245 | RFRPDC | DC RF error signal input |
| 246 | RFRPAC | AC RF error signal input |
| 247 | HRFZC | High-frequency RF signal zero crossover checking |
| 248 | CRTPLP |  |
| 249 | RFGND | RF grounding |
| 250 | CEQP |  |
| 251 | CEQN |  |
| 252 | OSP |  |
| 253 | OSN |  |
| 254 | RFGC |  |
| 255 | IREF | Reference current |
| 256 | AVDD3 | Analogue 3.3V power supply |

### Ⅱ.BA5954

BA5954 is a piece of servo drive single-piece integrated circuit, with built-in 4-channel BTL drive circuit. It can receive directly the PWM control signal output by digital servo IC, and with internal wave filter and drive amplifier, it pushes the execution part in the servo mechanism to accomplish the focusing, tracking, feed and main shaft drives. BA5954 adopts the packaging of 28 pins.

Note: The 28 pins of BA5954 are for outputting effective control signal, which is provided by the 50 pins of MT1389. When the signal is in high power level, BA5954 output is in validity, while the signal is in low power level, BA5954 will not be activated, and its output ports are in the state of cutoff.

The functions of pins of BA5954 are as the following table:

| Pin | Name | Function |
| --- | --- | --- |
| 1 | VINFC | Focusing control signal input |
| 2 | CF1 | External feedback loop |
| 3 | CF2 | External feedback loop |
| 4 | VINSL+ | Forward control input, connected to the reference voltage |
| 5 | VINSL- | Main shaft control signal input |
| 6 | VOSL | External feedback resistance |
| 7 | VINFFC | Focusing feedback signal input |
| 8 | VCC | 5V power supply |
| 9 | PVCC1 | 5V power supply |
| 10 | PGND | Grounding |
| 11 | VOSL- | Main shaft drive inverse voltage output |
| 12 | VO2+ | Main shaft forward voltage output |
| 13 | VOFC- | Focusing drive inverse voltage output |
| 14 | VOSC+ | Focusing drive forward voltage output |
| 15 | VOTK+ | Tracking drive forward voltage output |
| 16 | VOTK- | Tracking drive inverse voltage output |
| 17 | VOLD+ | Feed drive forward voltage output |
| 18 | VOLD- | Feed drive inverse voltage output |
| 19 | PGND | Grounding |
| 20 | VINFTK | Tracking feedback signal input |
| 21 | PVCC2 | 5V voltage |
| 22 | PREGND | Grounding |
| 23 | VINLD | Feed control signal input |
| 24 | CTK2 | External feedback loop |
| 25 | CTK1 | External feedback loop |
| 26 | VINTK | Tracking control signal input |
| 27 | BIAS | 1.4 reference voltage input |
| 28 | STBY | Enabling control signal |

### III. 29LV160BE

29LV160BE is a type of 16Mbit FLASH memory manufactured via 0.23um technology, with 16 byte width DQ0-DQ15, memory capacity of 16M bit, operation voltage of 3.3V, and packaging method of 48 pins TSOP. The specific operation mode is as the following table:

| Operation status | CE | OE | WE | RESET | A0~A19 | DQ0~QD7 | DQ8~DQ15 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | BYTE：high level | BYTE: Low level |
| Read | L | L | H | H | Ain | Dout | Dout | High resistance |
| Write | L | H | L | H | Ain | Din | Din | High resistance |
| Waiting | H | × | × | H | × | high resistance | high resistance | high resistance |
| Output forbidden | L | H | H | H | × | High resistance | High resistance | High resistance |
| Reset | × | × | × | L | × | High resistance | High resistance | High resistance |

The functions of pins of 29LV160BE are as the following table:

| Pin | Name | Function |
| --- | --- | --- |
| 15 | RY/BY | Ready/system is busy |
| 1~9、16~25 、48 | A0~A19 | 20-byte address bus |
| 26 | CE | Chip enabling |
| 27、46 | VSS | Grounding |
| 28 | OE | Output enabling |
| 29~36、38~44 | DQ0~DQ14 | 15-byte data bus |
| 37 | VCC | 5V power supply |
| 45 | DQ15/A-1 | Character extension mode as the data line; byte expansion mode as the address line |
| 47 | BYTE | Adopting 8-byte (in low level) or 16-byte output mode (in high level) |
| 11 | WE | Write enabling |
| 12 | RESET | Reset, valid in low level |
| 10、13、14 | NC | Neutral pin |

### IV. AE45164016

AE45164016 is a type of 64Mb (4Banks×1M×16bit) CMOS synchronization DRAM, featured with large memory and high speed. Its operation power voltage is 3.0V~3.6V, and it is packaged in 54-pin TSOP.

The functions of pins of AE45164016 are as the following table:

| Pin | Name | Function |
| --- | --- | --- |
| 1、14、27 | VDD | +3.3V power supply |
| 2、4、5、7、8、10、11、 13、42、44、45、47、48、 50、51、53 | DQ[0~15] | 16-byte data bus |
| 3、9、43、49 | VDDQ | +3.3V power supply |
| 6、12、46、52 | VSSQ | Grounding |
| 28、41、54 | VSS | Grounding |
| 15 | LDQM | Data I/O shielding signal |
| 16 | WE | Write control signal |
| 17 | CAS | Column address gate signal |
| 18 | RAS | Row address gate signal |
| 19 | CS | Chip selection signal |
| 20 | SD-BS0 | Section address 0 gate signal |
| 21 | SD-BS1 | Section address 1 gate signal |
| 22~26、29~35 | MA[0~11] | 12-byte address bus |
| 36、40 | NC | Neutral pin |
| 37 | CKE | Clock enabling signal |
| 38 | CLK | System clock input |
| 39 | UDQM | Data I/O shielding signal |

V. Pin Functions of TAS5508

TAS5508 is a high performance audio signal processing IC provided by TI. It has 8-channel PWM processing function, perfect protective functions, low distortion degree and excellent dynamic characteristics.

| 1 | VRA_PLL | Provide 1.8V reference voltage for PLL |
| --- | --- | --- |
| 2 | PLL_FLT_RET | PLL external filtering circuit |
| 3 | PLL_FLTM | PLL inverted input pin |
| 4 | PLL_FLTP | PLL non-inverted output pin |
| 5 | AVSS | Analog grounding |
| 6 | AVSS | Analog grounding |
| 7 | VRD_PLL | Provide 1.8V reference voltage for PLL |
| 8 | AVSS_PLL | PLL analog grounding |
| 9 | AVDD_PLL | PLL provides 3.3V voltage |
| 10 | VBGAP | Provide 1.2 V reference voltage |
| 11 | RESET | System reset signal, valid in low level |
| 12 | HP_SEL | Microphone input/output selection |
| 13 | PDN | Switch-off voltage, valid in low level |
| 14 | MUTE | Software muting control, valid in low level |
| 15 | DVDD | 3.3V digital power supply |
| 16 | DVSS | Digital grounding pin |
| 17 | VR_DPLL | Provide 1.8V reference voltage for PLL |
| 18 | OSC_CAP | Oscillation capacitance |
| 19 | XTL_OUT | Crystal oscillation output pin |
| 20 | XTL_IN | Crystal oscillation input pin |
| 21 | RESERVED | Connect to digital grounding |
| 22 | TBASE_SEL | Connect to digital grounding |
| 23 | RESERVED | Connect to digital grounding |
| 24 | SDA | Digital signal |
| 25 | SCL | Clock signal |
| 26 | LRCLK | RF channel clock signal |
| 27 | SCLK | Audio clock signal |
| 28 | SDIN4 | Audio data input pin |
| 29 | SDIN3 | Audio data input pin |
| 30 | SDIN2 | Audio data input pin |
| 31 | SDIN1 | Audio data input pin |
| 32 | PSVC | Control PWM signal output |
| 33 | VR_DIG | 1.8V reference voltage of digital core |
| 34 | DVSS | Digital grounding |
| 35 | DVSS | Digital grounding |
| 36 | DVDD | 3.3Vdigital service voltage |
| 37 | BKND_ERR | Logic error control pin, valid in low level |
| 38 | DVSS | Digital grounding |
| 39 | VALID | Output PWM signal is displayed normally, valid in high level |
| 40 | PWM_M_1 | PWM signal output 1 |
| 41 | PWM_P_1 | PWM signal output 1 |
| 42 | PWM_M_2 | PWM signal output 2 |
| 43 | PWM_P_2 | PWM signal output 2 |
| 44 | PWM_M_3 | PWM signal output 3 |
| 45 | PWM_P_3 | PWM signal output 3 |
| 46 | PWM_M_4 | PWM signal output 4 |
| 47 | PWM_P_4 | PWM signal output 4 |
| 48 | VR_PWM | 1.8V reference voltage of PWM core |
| 49 | PWM_M_7 | PWM signal output 7 |
| 50 | PWM_P_7 | PWM signal output 7 |
| 51 | PWM_M_8 | PWM signal output 8 |
| 52 | PWM_P_8 | PWM signal output 8 |
| 53 | DVSS_PWM | Digital grounding for PWM signal |
| 54 | DVDD_PWM | 3.3V voltage for PWM signal |
| 55 | PWM_M_5 | PWM signal output 5 |
| 56 | PWM_P_5 | PWM signal output 5 |
| 57 | PWM_M_6 | PWM signal output 6 |
| 58 | PWM_P_6 | PWM signal output 6 |
| 59 | PWM_HPML | Headphone output PWM left channel |
| 60 | PWM_HPPL | Headphone output PWM left channel |
| 61 | PWM_HPMR | Headphone output PWM right channel |
| 62 | PWM_HPPR | Headphone output PWM right channel |
| 63 | MCLK | 3.3V clock input |
| 64 | RESERVED | Connect to digital grounding |

IV. IC TAS5112

IC TAS5112 is an audio power amplifier of high performance made by TI. Bridging with 6Ω loading, each channel can output 50W. It has 95DB dynamic range, low distortion degree and low rate of heat generation with power efficiency up to 90%. It also has functions of low-voltage protection, high-temperature protection, overflow protection, etc. At the same time, it has built-in driving power adjustment gate circuit. Basic functions of its pins are as shown in the following table:

| Pin | Name | Function |
| --- | --- | --- |
| 31 | BST_A | Auxiliary power |
| 42 | BST_B | Auxiliary power |
| 43 | BST_C | Auxiliary power |
| 54 | BST_D | Auxiliary power |
| 23 | DGND | Digital input output reference |
| 16 | DREG | Digital service voltage adjustment circuit |
| 12 | DREG_RTN | Digital service voltage adjustment circuit |
| 25 | DVDD | Input output reference |
| 1，2，22，24，28，29，27，36，37，48，49，56 | GND | Grounding |
| 3，26 | GREG | Driving voltage adjustment of gate circuit |
| 30，55 | GVDD | Digital voltage adjustment |
| 15 | M1(TST0) | Mode selection |
| 14 | M2 | Mode selection |
| 13 | M2 | Mode selection |
| 4 | OTW | Protective pin in the high temperature |
| 34，35 | OUT_A | Output pin A |
| 38，39 | OUT_B | Output pin B |
| 46，47 | OUT_C | Output pin C |
| 50，51 | OUT_D | Output pin D |
| 32,33 | PVDD_A | Service voltage of half bridge A |
| 40,41 | PVDD_B | Service voltage of half bridge B |
| 44,45 | PVDD_C | Service voltage of half bridge C |
| 52,53 | PVDD_D | Service voltage of half bridge D |
| 20 | PWM_AM | Inverted input pin |
| 21 | PWM_AP | Non-inverted input pin |
| 18 | PWM_BM | Inverted input pin |
| 17 | PWM_BP | Non-inverted input pin |
| 10 | PWM_CM | Inverted input pin |
| 11 | PWM_CP | Non-inverted input pin |
| 8 | PWM_DM | Inverted input pin |
| 7 | PWM_DP | Non-inverted input pin |
| 19 | RESET_AB | Reset signal , valid in low level |
| 9 | RESET_CD | Reset signal , valid in low level |
| 6 | SD_AB | Signal switch off control |
| 5 | SD_CD | Signal switch off control |

IIV. IC SE5532

IC SE5532 is an amplified IC with dual channels and low noise. Compared to most other amplified ICs, it has lower noise, better output performance and power bandwidth. Its main features are: small-signal bandwidth; its direct voltage gain can be up to 50000 and alternating voltage gain can be up to 2200 under 10KHz; its power bandwidth can be up to 140KHz; relatively larger power supply range; fast slewing rate. Basic functions of its pins are as shown in the following table:

| Pin | Name | Function description |
| --- | --- | --- |
| 1 | OUTPUT-A | Output channel A |
| 2 | INVERTING INPUT-A | Inverted input A |
| 3 | NON-INVERTING INPUT-A | Non-inverted input A |
| 4 | V- | Negative power supply |
| 5 | NON-INVERTING INPUT-B | Non-inverted input B |
| 6 | INVERTING INPUT-B | Inverted input B |
| 7 | OUTPUT-B | Output channel B |
| 8 | V+ | Positive power supply |

IIIV、CS 5340

CS 5340 is an IC of analog/digital conversion; it can be applied to sample, analog-to-digital conversion and filter. During continuous input, its sampling frequency can be up to 200KHz. Its main features are as follows:

24 bytes conversion; supported audio frequency can be up to 192KHz; under power of 5V, its dynamic range can be up to 101DB; it has high pass filter to filter direct current. Functions of its pins are as follows:

| Pins | Name | Function description |
| --- | --- | --- |
| 1 | M0 | Mode selection |
| 16 | M1 | Mode selection |
| 2 | MCLK | Master clock signal |
| 3 | VL | Logic voltage power supply |
| 4 | SDOUT | Audio data output |
| 5，14 | GND | Grounding |
| 6 | VD | Digital power |
| 7 | SCLK | DRAM clock signal |
| 8 | LRCK | RF clock signal |
| 9 | RST | Reset signal |
| 10 | AINL | Analog input |
| 12 | AINR | Analog input |
| 11 | VQ | Quiescent voltage |
| 13 | VA | Analog power |
| 15 | FILT+ | Reference voltage |

##### Schematic & PCB wiring diagram

Decode board schematic & PCB wiring diagram

Amplifer board schematic & PCB wiring diagram

FRONT PANEL schematic & PCB wiring diagram

Power board schematic & PCB wiring diagram

Input & output board schematic & PCB wiring diagram

Spare parts list

Decode board

Amplifier board

POWER BOARD

FRONT PANNEL

INPUT & OUTPUT BOARD

# Text boxes

SF-HD62

SF-HD60

Radio reception head

16M ROM

SDRAM

Sany

deck

deck

芯

focus

track

feed

main

load

load drive

Power

Panel

status

Audio D/A，power大

Refor

Servo drive

Digital servo

Digital signal

MPEG decoder

AV output circuit

composite

S terminal

Y/Cb/Cr

6-way audio output

fiber, coaxial

MT1389

BA5954

4340，7265

HCU04

AT24C02

29LV160BE

Progressive

Y/Pb/Pr

VGA

Figure 1

CLK

DQML

DQMH

CKE

113

RAS

CAS

CS

WE

BA0

BA1

15

39

38

37

18

17

19

16

20

21

137

156

157

140

139

142

138

145

143

DMA0—DMA11

DQ0—DQ15

77

A0—A21

AD0—AD7

DCE

DRD

DWR

RY/BY

BYTE

AE45164016

MT1389

29LV160BE

26

28

11

15

47

79

66

VD

GND

Figure VII

U401

IC 0793

VFD

display

Keystroke

control

U201

MT1389

Remote

receiving

Panel indicator control

VFDST

VFDCK

VFDAT

No picture, no sound, no VFD display

Check if power supply of MT1389 3.3V, 1.8V is right?

Check the voltage of power board, and check if the decoding board is short circuit to the grounding.

If the clock signal output XO and XI is right?

Check if clock oscillating circuit 27M crystal oscillator, C275, C276, R224, R248 are damaged?

Check if reset signal URST# is in 5V high level?

Check if the reset circuit which is comprised by HCU04 and Q204 etc. is in working order?

Check if I2C bus, SDA, SCL 3.3V voltage is right?

Check if the AT24C16, CS4360, MT1389 SDA and SCL are short circuit to grounding, if R259 and R260 are in working order?

Check if SDRAM CLK, CS, RAS, CAS, WE communication signals are right?

Check if FLASH ROM, URST, DCE, DRD, DWR signals are right?

Check if the connection between MT1389, FLASH, SDRAM is right?

Check if the MT1389, SDRAM and FLASH are damaged?

Do not read disc

Check if the connection from BA5954 to MT1389 is open circuit

Check if the feed control input of BA5954 Pin 23 is 1.4V?

Check if the laser head has feed action.

Check feed motor and its connection.

Check if BA5954 pin 17,18 have 2.5V voltage output?

Check if BA5854 and the power supply 5V are in working order?

Check if the connection from BA5954 to MT1389 is open circuit?

Check if laser head has focus action?

Check if BA5954 pin 1 has focus control voltage input of 1.4V.

Check if the voltage output of BA5954 pin 13 and 14 are 2.5V?

Check focus coil and its connection.

Check if BA5854 and 5V power supply are in working order?

Check if the signal voltage of LD01, LD02 is 3.2V?

Check if there is laser coming out from laser head?

Check MT1389 and its connection

Check if V301 and V302 electron collector voltage is 2.3V?

Check if the laser head and its array line are right?

Check if the main shaft rotates?

Check if the control voltage of BA5954 pin 5 main shaft is 1.4V?

Check if the connection from BA5954 to MT1389 is open circuit?

Check if BA5954 or main shaft motor is damaged?

Check if BA5954 pin 11 and 12 output is 2.5V?

Check if MT1389 and its peripheral circuit is right?

Check if BA5854 and 5V power supply are in working order?