MA-2000S (RU) Service Manual

#### Content

Chapter One  Brief Introduction to Product	…………………………………….. 2

Section One  General Description	2

Section Two  Function and Feature	2

Chapter Two  Operating Principle…………………………………………………3

Section One  System Composing	3

Section Two  Operating Principle	3

2.1  Signal Processing Board	3

2.2  Panel	5

2.3  Power Amplifier Board	5

Appendix ……………………………………………………………………………..7

Appendix 1.  Schematic Diagram	7

Appendix 2.  Introduction to Main IC Pin Function……	11

Material lists

# Chapter One Brief Introduction to Product

## Section One  General Description

MA-2000S (RU) is a set of home theatre system composed of active 5.1CH satellite speakers with brand-new appearance and dual decoder. This system includes an external decoder, a subwoofer speaker with new appearance and the same five satellite speakers. The decoder is with DOLBY, DTS digital signals decoding function; stereo audio signal, coaxial and optical digital signal input function; and digital tuning function. 5.1CH audio output connects with active speaker directly. The main speaker of 5.1CH active speaker is subwoofer speaker, with 5.1CH power amplifier which outputs and connects with 5CH satellite speaker. This product is with complete function; overall silvery metal sense of reality; the massive mirror surface of the front side of decoder matches with electroplating outline border; character display matches with light, fashionable in appearance and special design in 5-direction button.

## Section Two  Function and Feature

2.1 One-way optical digital signal input

2.2 Two-way coaxial digital signal input

2.3 Two-way stereo audio signal input

2.4 DTS, DOLBY, DOLBY Pro. LogicⅡ decode function

2.5 Built-in channel noise test function

2.6 Four preset digital sound field processing (DSP)

2.7 Separate level adjustment to multi-channel

2.8 High, low tone adjustment function

2.9 Auto mute function when no signal

2.10 With standby function

2.11 Digital tuning function

2.12 Save and call radio station programs

2.13 Manual, auto searching function

2.14 Separate 5.1CH power amplifying

2.15 Full remote control operation

2.16 Short-circuit, over-voltage, over-current and over-heat protection function

# Chapter Two Operating Principle

## Section One  System Composing

The electronic solution of MA-2000S (RU) is mainly composed of the following several modules (appendix diagram 1):

- Signal processing board: including switching power circuit, input selection circuit, DTS, DOLBY, DOLBY Pro. LogicⅡ decode and volume equalization;

- Panel: static VFD display, menu button and main volume control;

- Power amplifier board: linear power supply, separate 5.1CH power amplifying.

## Section Two: Operating Principle

### 2.1 Signal processing board

2.1.1 Operating principle for power supply

Power supply of decode board adopts switching power supply, and its schematic diagram is shown as follows (appendix figure 2):

Schematic diagram for switching power circuit

220V AC electric supply is added to integrated bridge rectification circuit through common mode rejection inductor L122. 311V DC outputted after bridge rectification is individually added to two transformers through TC501 filtering, and then sent to DRAIN control pin of switching module U501 and U502.

The power operating voltage of IC supplies for IC working after being filtered through rectification directly and voltage-divided through resistor. Diode D508, capacitor C516 and resistor R516 compose absorption circuit, which provides the discharge return circuit of reverse electromotive for transformer 1-4 winding. The FB pin controlling IC is feedback control pin, which decides the conduction of pulse width and time limit according to its current to ensure the stability of output voltage.

Decode is with the function of DC power on and off:

When the machine connects with power supply, the output voltage of transformer generates a 76V high frequency voltage in the pole of controllable silicon V117A through VD112 self-wave rectification, and meanwhile couples to a same high frequency voltage in the pole of V117G through capacitors C279 and R262. Due to the effect of feedback voltage stabilization, a stable 5V DC voltage is achieved in pole of V117K. As a result of conduction of controllable silicon, 76V voltage decreases to about 7V. All other secondary winding has no output. Power board only has CPU5V output and power is in standby working mode.

When standby changes to power-on mode, 39 pin of panel IC TP6317 outputs a high level to make the conduction of triode V116 and give a low level to G pole of V117. Controllable silicon V117 is cut off and other winding begins normal working.

2.1.2 Signal processing board

1. Input selection circuit (appendix figure 3)

MA-1000S has 5 kinds of input means: optical input, coaxial input, CD, DVD and tuning input.

Digital signals of optical and coaxial input are processed by decode board. The analog input selection of MA-1000S is fulfilled through electronic switch IC N117 CD4052, and its truth value table is shown as follows:

|  | CD | DVD | Tuning |
| --- | --- | --- | --- |
| A | 0 | 1 | 0 |
| B | 0 | 0 | 1 |

After the analog signal of MA-1000S passing N117, selected through IC N118 CD4052 and then sent to volume and equalization control IC N119 M62446. After signals being processed by M62446, outputted to power amplifier board for amplifying.

2. Decoding part circuit (appendix figure 4)

Material list for main components of decoding part (appendix 2):

CUP: control unit of the whole machine (appendix figure 5)

IC 493264: high-performance digital audio decoding, including DOLBY decoding, DTS decoding and DSP processing

IC 8415: series audio digital signal receiving

IC CS5340: 2-channel A/D conversion

IC CS 4360: 6-channel D/A conversion

IC 24C02: state memory

IC 74HC04: multi-path inverter

IC BM1117-3.3: 3.3V voltage regulating IC, providing power for CS8415 and CS4923.

Operating principle:

After optical and coaxial signal being filtered through inductor and capacitor, opposite phased through inverter, and then sent to the signal input pin 4, 12 and 14 of series audio digital signal receiving IC CS8415. After passing through this IC, series audio digital signals converse into PCM signals, sending from 16 (sampling rate signal), 17 (main channel clock signal) and 18 (audio data signal) pin of this IC to 25 (sampling rate control signal), 26 (clock signal) and 22 (PCM data input port 1) pin of digital audio decode IC, and then perform data processing.

Signals of left and right channel of analog signal are sent to decode board after passing through XS17. After being processed by front-stage small signals, signals are sent to 10 and 12 pin of IC CS5340 to perform A/D conversion, changing analog audio signal to PCM signal and then sending from 4 (audio PCM signal), 17 (sampling rate signal) and 18 (clock signal) pin of CS5340 to 27, 28 and 29 pin of CS4923, that is, inputting from another PCM input port of CS4923 to perform data processing.

Therefore, digital sound field processing of analog signal is relatively independent from coaxial and optical signals’ processing. If working of some kind of way is abnormal, the possibility of having trouble before CS4923 is more.

CS4923 is with strong digital sound field processing function. All DSP processing, PROII processing and DOBLY/AC-3 processing are performed inside through being controlled by CPU.

Audio PCM signals after being processed by CS 4923 are send to CS 4360 to perform D/A conversion, reverting PCM signals into 6CH analog signals, then filtering the noise outside frequency range through a band-pass filter, and then sending to input selection part to perform selection input.

### 2.2 Panel

Panel is mainly composed of VFD screen, drive IC TP6317, IR sensor and indicator display circuit which mainly fulfill functions of man-machine conversation and working mode display.

The composed frame diagram is shown as follows (appendix figure 6):

Through three controlling lines DTS, DCK, DDA, CPU controls TP6317 to display whole machine working state, and receive the user control order sent by TP6317. Control the controlled circuit of whole machine to make the machine work in indicated state.

When users are operating panel buttons, through keyboard scanning circuit, controlled order is sent to TP6371 controlled order. After TP6317 coding driving inside, it outputs data to CPU which fulfills the control of controlled circuit and controls VFD display through TP6371.

VFD101 is vacuum fluorescent display screen with the most obvious feature of high brightness. The 1, 2, 19, 20 pin is filament power supply; through controlling TP6317, CPU controls display of screen to make characters of corresponding working mode display on screen.

Remote control receiving circuit is mainly composed of remote control receiving head, among which the 2nd pin is grounding, the 3rd pin is power-supplying end and the 1st pin is signal output pin that outputs to CPU directly. CPU controls the corresponding circuit according to received signals.

### 2.3 Power amplifier board

2.3.1 Part of power supply (appendix figure 7)

Power amplifier power adopts liner power supply. After being rectified through rectification diode VD100~VD103 and capacitor C170, C171, filter and output +28V, -28V voltage to supply for power amplifying IC 7296; After being rectified through rectification diode VD104~VD107 and capacitor C160, C161, filter and output +18V, -18V voltage to supply for power amplifying IC 7265.

2.3.2 Part of power amplifying

6CH audio signal is processed through decoder and inputted to power amplifying circuit by Q-link to perform amplifying individually. Signals of main channel, surround channel and center channel are amplified by three integrated power IC TDA7256. Signal of subwoofer is amplified by one integrated IC TDA7296.

The used IC (TDA7265) has the following features (attached with TDA7256 data):

- Complete protection circuit: shored to earth protection, over-heat protection;

- Voltage range of power supply: ±5～±25V;

- Casing: bi serial 11 pins casing;

- Power: 2*25W (8Ω);

- With mute function.

The used IC (TDA7265) has the following features (attached with TDA7296 data):

- Voltage range:±35V；

- Power: 60W (4Ω);

- With mute and standby function;

- Complete protection circuit: over-current protection, over-heat protection;

- Casing: bi serial 15 pins casing

2.3.3 Anti impulsive sound circuit when power on and off (TDA7296)

When power on, the process of “standby → mute → work” fulfilled by delay circuit has effectively eliminated the power-on impulsive sound. When power off, the process of “standby → mute → work” fulfilled by delay circuit has effectively eliminated the power-off impulsive sound.

# Appendix

## Appendix 1 Schematic diagram

Figure 1 MA-1000S functional block diagram

Figure 2 Schematic diagram for power

Figure 3 Schematic diagram 1 for signal processing board

Figure 4 Schematic diagram 2 for signal processing board

Figure 5 Schematic diagram 3 for signal processing board

PCB for signal processing board

Figure 6 Schematic diagram for panel

PCB for panel

Figure 7 Schematic diagram for Power amplifier board

PCB for Power amplifier board

## Appendix 2  Function introduction to main IC pins:

1. CS4360

CS4360 is a 6CH audio DAC (Digital-to-Analog Conversion) produced by CIRRUS LOGIC Company. Digital volume adjustment may be fulfilled through software. The adjustment factor of each step is 1dB, and with 119 dB attenuation range. Adopt +3.3V or +5V voltage to supply power. 28 pins casing and the main features are :

① 24-bit sampling accuracy

② The highest 192KHZ sampling rate

③ Dynamic range: 102dB

④ SNR: -90 dB

⑤ Low power consumption: In +3.3V voltage operating mode, power consumption is 105mW

Pin function of CS4360 is shown as follows:

| Pin | Name | Function | Pin | Name | Function |
| --- | --- | --- | --- | --- | --- |
| 1 | VLS | Series audio power supply, +3.3V | 15 | M2 | Mode 2 |
| 2 | SDIN1 | Series audio data 1 input | 16 | FILT+ | In-phase feedback voltage output |
| 3 | SDIN2 | Series audio data 2 input | 17 | VQ | Static operating voltage connects with filter externally |
| 4 | SDIN3 | Series audio data 3 input | 18 | MUTEC3 | Output 3 static control |
| 5 | SCLK | Bit clock | 19 | AOUTB3 | Analog audio 3 output |
| 6 | LRCK | Left/right channel clock | 20 | AOUTA3 | Analog audio 3 output |
| 7 | MCLK | Main clock input | 21 | GND | Ground |
| 8 | VD | Digital power supply, +3.3V | 22 | VA | Analog power supply, +5V |
| 9 | GND | Ground | 23 | AOUTB2 | Analog audio 2 output |
| 10 | RST | Reset input | 24 | AOUTA2 | Analog audio 2 output |
| 11 | SCL | Series control clock | 25 | MUTEC2 | Output 2 static control |
| 12 | SDA | Series control data | 26 | AOUTB1 | Analog audio 1 output |
| 13 | CS/M1 | Chip selection/mode 1 | 27 | AOUTA1 | Analog audio 1 output |
| 14 | VLC | Control port power supply, +3.3V | 28 | MUTEC1 | Output 1 static control |

2. CS 4923

CS4923 is a digital processing IC, including DOLBY decoding, DTS decoding and DTS processing, etc. The function of its main pins is as follows:

PIN 30: Main clock input port

PIN 31: DSP clock select internal clock when port is low.

PIN 8－11, 14－17: Data address output and data input port

PIN 7: Clock input port of I2C-way communication

PIN 19: Data input port of I2C-way communication

PIN 5: Address, data input/output latching port

PIN 21: External recorder selection port

PIN 36: Reset input port

PIN 22: PCM audio data input port 1

PIN 27: PCM audio data input port 2

PIN 25, 28: PCM audio data input bit clock port 1, 2

PIN 26, 29: PCM audio data sampling rate input port

PIN 42: Audio data sampling rate output port

PIN 39, 40, 41: Digital audio output port

PIN 43: Audio data output bit clock

PIN 44: Audio main clock

3. CS5340

CS5340 is a 2CH A/D switching IC whose function is to switch analog signal into PCM signal to make CS4923 perform digital sound field processing. The function of its main pins is as follows:

PIN1, PIN16: Mode selection

PIN2: Audio main clock

PIN3: Digital signal input/output power supply

PIN4: Audio data output

PIN5, PIN14: Grounding pin

PIN6: Digital power supply

PIN7: Sampling rate control

PIN8: Left/right clock signal

PIN9: Reset signal

PIN10, PIN12: simulate signal input

PIN13: Simulate part of power supply

PIN15: Positive sequence reference voltage

- CS 8415

PIN1: Control input/output data line

PIN2: Byte control

PIN4, PIN5: Serial audio signal input port

PIN12-15, PIN25, 26：Serial audio signal input port

PIN6: Power supply

PIN9: Reset signal

## MATEARIAL LISTS

signal processing board

pannel

power amplifier board

# Text boxes

N100

TP6317

VFD display

Buttons control

# CPU

Remote control receiving

Panel indicator control zone

DDA

DCK

DST

Common mode Rejection

Rectification

Switching circuit

Rectification circuit

Filter circuit

Driver circuit

Output testing

Input circuit

Control circuit

Output circuit

Change circuit